## Slide 1: Introduction to ROS
2020. 03. 30. ~ 2020.04.10

## Slide 2: Contents
Introduction to ROS
ROS Core Concepts
  Node, Message, Topic, ROS Master, Parameter Server
ROS Basic Commands
  roscore, rosrun, rosnode, rostopic
Tutorials: WritingPublisherSubscriber
ROS Installation
Practice with RRBot
Experiments Guideline

## Slide 3: Introduction to ROS
What is ROS?
  ROS is an open-source robot operating system
  A set of software libraries and tools that help you build robot applications that work across a wide variety of robotic platforms
  Originally developed in 2007 at the Stanford Artificial Intelligence Laboratory and development continued at Willow Garage
  Since 2013 managed by OSRF (Open Source Robotics Foundation)

## Slide 4: Introduction to ROS
ROS Main Features
  The operating system side, which provides standard operating system services such as
    hardware abstraction
    low-level device control
    implementation of commonly used functionality
    message-passing between processes
    package management
  A suite of user contributed packages that implement common robot functionality such as SLAM, planning, perception, vision, manipulation, etc.

## Slide 5: Introduction to ROS
Robots using ROS

## Slide 6: ROS Core Concepts
ROS Nodes
  Single-purposed executable programs
    sensor driver, actuator driver, mapper, planner, UI, etc
  Individually compiled, executed, and managed
  Nodes are written using a ROS client library
    roscpp – C++ client library
    rospy – python client library
  Nodes can publish or subscribe to a Topic
  Nodes can also provide or use a Service

## Slide 7: ROS Core Concepts
ROS Topics
  A topic is a name for a stream of messages with a defined type
    e.g., data from a laser range-finder might be sent on a topic called scan, with a message type of LaserScan
  Nodes communicate with each other by publishing messages to topics
  Publish/Subscribe model: 1-to-N broadcasting

## Slide 8: ROS Core Concepts
ROS Graph

## Slide 9: ROS Core Concepts
ROS Messages
  Strictly-typed data structures for inter-node communication
  For example, “geometry_msgs/Twist” is used to express velocity commands:
    Vector3 is another message type composed of:

## Slide 10: ROS Core Concepts
ROS Master
  Provides connection information to nodes so that they can transmit messages to each other
    Every node connects to a master at startup to register details of the message streams they publish, and the streams to which that they to subscribe
    When a new node appears, the master provides it with the information that it needs to form a direct peer-to-peer connection with other nodes publishing and subscribing to the same message topics
1. “Camera” node initialization
2. “Image viewer” node initialization
3. Start transferring images to Image viewer node

## Slide 11: ROS Core Concepts
Parameter Server
  A shared, multi-variate dictionary that is accessible via network APIs
  Nodes use this server to store and retrieve parameters at runtime.
  Runs inside the ROS master

## Slide 12: ROS Basic Commands
“roscore”
  “roscore” is the first thing you should run when using ROS
  Usage:
  “roscore” will start up:
    A ROS Master
    A ROS parameter server
    A rosout for logging node

## Slide 13: ROS Basic Commands
“rosrun”
  “rosrun” allows you to run a node
  Usage:
  Example:

## Slide 14: ROS Basic Commands
Demo - Turtlesim

## Slide 15: ROS Basic Commands
“rosnode”
  Displays debugging information about ROS nodes, including publications, subscriptions and connections
Command | Function
rosnode list | List active nodes
rosnode list | Test connectivity to node
rosnode info | Print information about a node
rosnode kill | Kill a running node
rosnode machine | List nodes running on a particular machine

## Slide 16: ROS Basic Commands
“rostopic”
  Gives information about a topic and allows to publish messages on a topic
Command | Function
rostopic list | List active topics
rostopic echo /topic | Prints messages of the topic to the screen
rostopic info /topic | Print information about a topic
rostopic type /topic | Prints the type of messages the topic publishes
rostopic pub /topic type args | Publishes data to a topic

## Slide 17: ROS Basic Commands
Publish to ROS topic
  Use the rostopic pub command to publish messages to a topic
  For example, to make the turtle move forward at a 0.2m/s speed, you can publish a “cmd_vel” message to the topic “/turtle1/cmd_vel”:
  For example, to make the turtle turn in circles continuously, type:

## Slide 18: ROS Basic Commands
Publish to ROS topic
  Use the rostopic pub command to publish messages to a topic
  For example, to make the turtle move forward at a 0.2m/s speed, you can publish a “cmd_vel” message to the topic “/turtle1/cmd_vel”:
  For example, to make the turtle turn in circles continuously, type:

## Slide 19: Catkin Build System
“catkin” Build System
  “catkin” is the ROS build system
    The set of tools that ROS uses to generate executable programs, libraries and interfaces
  The original ROS build system was “rosbuild”
    Still used for older packages
  Implemented as custom CMake macros along with some Python code

## Slide 20: Catkin Build System
“catkin” Workspace
  A a set of directories in which a set of related ROS code lives
  You can have multiple ROS workspaces, but you can only work in one of them at any one time
  Contains the following spaces:
Source Space | contains the source code of catkin packages. Each folder within the source space contains one or more catkin packages.
Build Space | is where CMake is invoked to build the catkin packages in the source space. CMake and catkin keep their cache information and other intermediate files here.
Development Space (Devel) | is where built targets are placed prior to being installed
Install Space | Once targets are built, they can be installed into the install space by invoking the install target.

## Slide 21: Catkin Build System
Creating a “catkin” Workspace
  Creating a workspace
Building “catkin” Workspace
  “catkin_make” command builds the workspace and all the packages within it

## Slide 22: Catkin Build System
Creating a ROS Package
  Change to the source directory of the workspace
  “catkin_create_pkg” creates a new package with the specified dependencies
  For example, create a “first_pkg” package:
Building “catkin” Workspace
  “catkin_make” command builds the workspace and all the packages within it

## Slide 23: Tutorials: WritingPublisherSubscriber
“ros::Publisher”
  Manages an advertisement on a specific topic
  Created by calling “NodeHandle::advertise()”
    Registers this topic in the master node
  Example for creating a publisher:
    First parameter is the topic name
    Second parameter is the queue size
  To publish a message on a topic call “publish()”
    The message’s type must agree with the type given as a template parameter to the “advertise<>()” call

## Slide 24: Tutorials: WritingPublisherSubscriber
Talker and Listener
  We’ll now create a package with two nodes:
    “Talker” publishes messages to topic “chatter”
    “Listener” reads the messages from the topic and prints them out to the screen
  First create the package “chat_pkg”
  Add a C++ source files named “Talker.cpp” and “Listener.cpp”
  Copy the following code into it

## Slide 25: Tutorials: WritingPublisherSubscriber
“Talker.cpp”

## Slide 26: Tutorials: WritingPublisherSubscriber
Subscribing to a Topic
  To start listening to a topic, call the method “subscribe()” of the node handle
    This returns a Subscriber object that you must hold on to until you want to unsubscribe
  Example for creating a subscriber:
    1st parameter is the topic name
    2nd parameter is the queue size
    3rd parameter is the function to handle the message

## Slide 27: Tutorials: WritingPublisherSubscriber
“Listener.cpp”

## Slide 28: Tutorials: WritingPublisherSubscriber
Compile the Nodes
  Add the following to the package’s “CMakeLists.txt” file
  Now build the package and compile all the nodes using the “catkin_make” tool:
    This will create two executables, “talker” and “listener”, at “~/catkin_ws/devel/lib/chat_pkg”

## Slide 29: Tutorials: WritingPublisherSubscriber
Running the Nodes From Terminal
  Run “roscore”
  Run the nodes in two different terminals:
talker
listener

## Slide 30: Tutorials: WritingPublisherSubscriber
“rqt_graph”
  “rqt_graph” creates a dynamic graph of what's going on in the system
  Use the following command to run it:

## Slide 31: ROS Installation
Install ROS
  Ubuntu 16.04 : install ROS Kinetic
    http://wiki.ros.org/kinetic/Installation/Ubuntu
  Ubuntu 18.04 : install ROS melodic
    http://wiki.ros.org/melodic/Installation/Ubuntu
  !Only python2.7 version is compatible with ROS.
    Set default python version to 2.7
  Configuring Your ROS Environment
  Install ROS control package
    http://wiki.ros.org/ros_control
    sudo apt-get install ros-[kinetic or melodic]-ros-control ros-[kinetic or melodic]-ros-controllers sudo apt install ros-[kinetic or melodic]-controller-manager sudo apt-get install ros-[kinetic or melodic]-gazebo-ros-pkgs ros-[kinetic or melodic]-gazebo-ros-control

## Slide 32: Practice with RRBot
URDF (Univeersal Robotic Description Format)
  URDF is an XML file format used in ROS to describe all elements of a robot
  detail information of URDF : http://gazebosim.org/tutorials/?tut=ros_urdf
  Getting RRBot
  Examine the RRBot URDF
    Define your own robot model by referring this file
  View in Gazebo
 | metric
Wheel Radius | 0.1m
Wheel Width | 0.05m
Wheel Separation | 0.35m
Base Frame | 0.3m x 0.3m x 0.05m

## Slide 33: Practice with RRBot
Add the gazebo_ros_control_plugin
  The default plugin XML should be added to your URDF
  detail information of controller setting: https://bitbucket.org/osrf/gazebo_tutorials/src/default/ros_control/tutorial.md
Create a ros_controls package

## Slide 34: Practice with RRBot
Create a .yaml config file
  In the config folder of your MYROBOT\_control package, adapt the following RRBot example to your robot as MYROBOT_control/config/rrbot_control.yaml:

## Slide 35: Practice with RRBot
Create a roslaunch file
  Within the launch folder create a MYROBOT_control/launch/MYROBOT_control.launch file and adapt the following RRBot example to your robot:

## Slide 36: Practice with RRBot
Start the controllers using roslaunch
  Start the RRBot simulation:
  Load the controllers for the two joints by running the second launch file:
  Send example joint commands to them for testing:

## Slide 37: Experiments Guideline
1. Create URDF Model of below mobile robots
  Guideline
    cd ~/catkin_ws/src
    mkdir mobilerobot && cd mobilerobot
    catkin_create_pkg mobilerobot_description
    cd ~/catkin_ws/src/mobilerobot/mobilerobot_description/
    mkdir urdf && cd urdf
    [construct your model.urdf]
  To check urdf models
    sudo apt-get install liburdfdom-tool
    check_urdf model.urdf
    urdf_to_graphiz model.urdf
 | metric
Wheel Radius | 0.1m
Wheel Width | 0.05m
Wheel Separation | 0.35m
Base Frame | 0.3m x 0.3m x 0.05m

## Slide 38: Experiments Guideline
2. Adapt URDF model to gazebo simulation
  Guideline
    cd ~/catkin_ws/src/mobilerobot
    catkin_create_pkg mobilerobot_gazebo
    cd mobilerobot_gazebo
    mkdir launch && cd launch
    [construct your mobilerobot_urdf.launch]
3. Create controller
  Guideline
    cd ~/catkin_ws/src/mobilerobot
    catkin_create_pkg mobilerobot_control controller_manager joint_state_controller robot_state_publisher
    cd mobilerobot_control
    mkdir config && mkdir launch
    [create a .yaml file in config folder & create roslaunch file in launch folder]

## Slide 39: Experiments Guideline
4. Control mobile robot
  Guide line
    cd ~/catkin_ws
    catkin_make
    source devel/setup.bash
Terminal 1 : roslaunch mobilerobot_gazebo mobilerobot_urdf.launch
Terminal 2 : roslaunch mobilerobot_control mobilerobot_control.launch
Terminal 3 :

## Slide 40: Experiments Guideline
Submit Results & Reports
  Results
    Compress and submit your own ROS package (compress mobilerobot folder)
    Mobile robot controller video (wmv, encoding to 10MB or less)
  Reports
    (Description of robot control method and manufactured package) within 6 pages
    Reports should be as detailed as possible (Introduction, experimental process, results, conclusions)
  submit e-mail : tjsong@rit.kaist.ac.kr (assistant : TaekJin Song)
  submit e-mail in title : [RE510]Student_number-Name (ex : [RE510]20187022-송택진)
  submit file_name : StudentNumber_Name.zip (ex : 20187022_송택진.zip)
  - Submission deadline : 2020.04.10